## Slide 1: DA3 – Signed Binary Numbers
COMP 256 – Dickinson College
Prof. Braught
Spring 2023
Notes: Positive, negative and 0 whole numbers.

## Slide 2: Signed Binary Representations
Sign Magnitude
  Simple and intuitive
  Complicates hardware
Two’s Complement
  Less obvious and intuitive
  Simplifies hardware
Notes: More ”pie”!
As we will see…
The same bit string may represent two different signed whole numbers depending upon which interpretation we use.

## Slide 3: Sign Magnitude Representation
The most significant bit indicates the sign of the number.
  0 → positive
  1 → negative
The remaining n-1 bits give the value using unsigned binary representation.
Samples:
0010 10102SM
1010 10102SM
Value in
Unsigned Binary
4210
Positive
Number
Negative
Number
Value in
Unsigned Binary
- 4210
Notes: We can’t write + or – because we only have 1’s and 0’s
So let’s just use the MSb as the sign…
0 for +
1 for –
Then we’ll use unsigned binary for the rest of the bits to tell us what the number is
Will use 2SM subscript to indicate base 2 (binary) sign magnitude values.
- Remember, its just a byte until we know how to interpret it.
- Is it unsigned? Is it ASCII? Is it Unicode? Is it sign magnitude?
- We need to know!
- You don’t want to get a foot when you want a desert!
Notice that with 2SM we ignore the sign bit when computing the value.
- It tells us the sign, but it plays no role in computing the value.
Positive Number Example:
0010 1010 (2SM)
- It is positive
- Then use the remaining 7 bits for the value.
010 1010
(32 + 8 + 2)
42 (base 10).
Negative Number Example:
1010 1010 (2SM)
- It is negative
- Then use the remaining 7 bits for the value.
- Notice that they are the same 7 bits as above
010 1010
- So this must be 42
- But we know this value is negative
- So it is -42 (base 10).

## Slide 4: Sign Magnitude Representation
Give the 8-bit sign magnitude binary representation for these base 10 values:
Give the base 10 values for these sign magnitude binary values:
0110 10102SM
1011 00102SM
7310
-5210
Notes: Some practice.
Good chance to review your unsigned binary.

## Slide 5: Sign Magnitude Representation
Give the base 10 values for these sign magnitude binary values:
0110 10102SM
1011 00102SM
7310
-5210
110 10102
(64+32+8+2)10
10610
-011 00102
-(32+16+2)10
-5010
(64+8+1)10
0100 10012SM
-(32+16+4)10
1011 01002SM
Give the 8-bit sign magnitude binary representation for these base 10 values:
Notes: Solutions to the practice problems on the prior slide.
Note: For the base 10 -> Sign Magnitude examples
- The values to be summed can be found just as we did in examples in DA1.
- For example… for 73 (base 10)
- There is one 64 in 73
- So we need to represent 73-64 = 9 more.
- There are no 32’s or 16’s in 9.
- There is one 8 in 9
- So we need to represent 9 – 8 = 1 more.
- There are no 2’s in 1
- There is one 1 in 1.
- So we need to represent 1 – 1 = 0.
- Good! We got to 0.
The same could be done for representing 52.
- I took a short cut here and just wrote the values that are being summed.
- That is the minimum that I would expect at this point if you are writing a solution.

## Slide 6: Sign Magnitude Representation
Sign magnitude representation has some complications:
What are the base 10 values of the following sign magnitude numbers? 0000 00002SM
1000 00002SM
What is wrong with the following addition of sign magnitude numbers?
1 0010 11002SM
+ 1010 11002SM
1101 1000
Notes: Here are two of the complications:
- Sign magnitude contains two different representations of zero.
- There is positive zero and negative zero.
- Makes comparing to zero different than comparing to other numbers.
- x == 0 would have to do two different comparisons.
- That’s a special case
- Special cases in hardware make it more complicated
- Just like special cases in software (e.g. all those extra little if statements)
- When adding sign magnitude values, we have to account explicitly for the sign bit.
- Here we have added a positive number to its own negative (all the bits are the same except the sign)
- We should get 0 in this case, but we don’t even get close.
- So we would need to do binary addition differently for sign magnitude numbers than for unsigned numbers.
- The way we added unsigned binary numbers was pretty intuitive.
- So we would like to keep that if possible.
- If we were to sign magnitude arithmetic differently,
- Then we would need different circuits for adding unsigned binary and sign magnitude binary.
- That makes the hardware more complicated.
- Also, the circuits to do the sign magnitude arithmetic are complicated with lots of special cases.
- We could build them, and it has been done.
- But you’ll in a bit that using a different representation solves the problem more elegantly.

## Slide 7: Two’s Complement Representation
The most significant bit still indicates the sign of the number.
  0 → positive
  1 → negative
Positive numbers use unsigned binary representation.
The negative (i.e. complement) of a number is found by:
  Flipping the bits (0→1 or 1→0) and adding 1.
Samples:
0010 10102TC
Unsigned Binary
4210
Positive
Number
Negative
Number
- 4210
1
1101 0101
+ 1
1101 01102TC
What happens if we take the complement of a negative number?
Complement
(flip bits, add 1)
Notes: Using two’s complement representation addresses both of those complications.
- And everything just works the way it is supposed to…
- It’s just a little (or a lot) less intuitive.
I will use the 2TC subscript to indicate that a value is in two’s complement representaton.
For 0010 1010
- the MSbit is 0 so it is a positive number.
- Convert it to base 10 using unsigned binary.
- we get 42 base 10
- Note that this is the conversion that was shown on the second slide
- So, the details of why this is 42 are not shown again.
If we want to know what negative 42 is we take its complement.
- Flip all of the bits (0’s become 1’s and 1’s become 0’s)
- Add 1
- The resulting binary value is the representation of -42 base 10 in two’s complement.
If we take the complement of the two’s complement representation of -42 base 10
- flip the bits and add 1
0010 1001
+ 1
0010 1010
We get back to the representation of positive 42 base 10.
Which is just the way things are supposed to operate!
- Vey nice.
In the homework, you’ll explore a bit about the two quirks of unsigned binary…
- Does two’s complement have two zeros?
- Can we add positive and negative two’s complement numbers?

## Slide 8: 8-bit Two’s Complement Representation
Binary to Decimal Examples
1011 00112TC
0110 10102TC
Notes: Do these as worked examples.

## Slide 9: 8-bit Two’s Complement Representation
0100 1100
+ 1
0100 11012
Find the
complement
Binary to Decimal Examples
0110 10102TC
1011 00112TC
(64+32+8+2)10
10610
- (64+8+4+1)10
- 7710
Negative.
Positive
0110 10102
Use
unsigned
binary
Positive.
Use unsigned binary… but include a -
Notes: This slide animates the process of solving the two worked examples from the prior slide.
Included here for later reference.
For 0110 1010
- MSbit = 0 so these bits represent a positive number in two’s complement representation.
- Convert it to base 10 using unsigned binary
For 1011 0011
- MSbit = 1 so these bits represent a negative number in two’s complement representation.
- So find the complement (i.e. its positive)
- Flip the bits & add 1
- Then convert the positive to base 10 using unsigned binary
- Add the negative sign to get the correct negative base 10 value.

## Slide 10: Two’s Complement Representation
0011 10012TC
1110 01112TC
Give the base 10 values for these
8-bit two’s complement binary values.
Notes: Some additional practice as time permits.
- If time is tight we’ll skip to the base 10 -> 2TC conversion examples
- Then come back to these at the end for the rest of class.
Now,
- How could we get the 2TC representation of
- Negative 57?
- Positive 25?

## Slide 11: Two’s Complement Representation
0011 10012TC
Give the base 10 values for these
8-bit two’s complement binary values.
(32+16+8+1)10
5710
0011 10012
Positive 2TC.
So, use unsinged
binary.
0001 1000
+ 1
0001 10012
Negative 2TC.
So, find complement.
1110 01112TC
- (16+8+1)10
- 2510
Then use unsigned binary with a negative sign.
Notes: This slide animates the solution of the practice exercises on the prior slide.
Included here for later reference.
For 0011 1001
- MSbit is 0 so it represents a positive base 10 value.
- just use unsigned binary representation.
For 1110 0111
- MSbit is 1 so it represents a negative base 10 value.
- Take the complement so we can deal with a positive value
- Flip the bits, add 1
- Convert to base 10 using unsigned binary
- Add back in the negative sign.

## Slide 12: 8-bit Two’s Complement Representation
Decimal to Binary Examples
9810
- 10210
Notes: Do these in class as worked examples.

## Slide 13: 8-bit Two’s Complement Representation
1001 1001
+ 1
1001 10102TC
Find the
complement to get -102
Decimal to Binary Examples
0110 00102TC
(64+32+2)10
9810
- 10210
Negative.
0110 00102
Positive.
Just use
unsigned
binary
0110 01102
Positive 102.
But we need
the negative.
(64+32+4+2)10
10210
Work with
the positive
instead.
Notes: Animates the previous worked examples for later reference.
For 98 base 10
- It is a positive value
- so just use unsigned binary.
For -102 base 10
- It is a negative value
- So we will work with positive 102 then correct the sign at the end.
- Convert 102 to unsigned binary
- Take the complement to make it negative.
- Remember to get the complement we flip the bits and add 1.
- Gives us the 2TC representation of -102.

## Slide 14: Two’s Complement Representation
8810
-3510
Give the 8-bit two’s complement binary representations for these base 10 values.
Notes: Some practice problems as time permits.

## Slide 15: Two’s Complement Representation
8810
-3510
Give the 8-bit two’s complement binary representations for these base 10 values.
0101 10002
(64+16+8)10
(32+2+1)10
0101 10002TC
Positive.
Just use
unsigned
binary
Negative.
3510
Work with
the positive
instead.
0010 00112
Positive 35.
But we need
the negative.
1101 1100
+ 1
1101 11012TC
Find the
complement to get -35.
Notes: Animations of the practice problems from the previous slide.
For 88 base 10
- it is positive
- so just convert using unsigned binary.
For -35 base 10
- it is negative so work with the positive and then take the complement.
- Convert positive 35 to unsigned binary
- Find the complement
- Flip the bits, add one
- Gives us the two’s complement representation of -35 base 10.

## Slide 16: Acknowledgments
https://creativecommons.org/licenses/by/4.0/
Slide Template From:
Slide Content Licensed as:
Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.
Notes: Note: Individual images may be covered by their own licensing agreements and were incorporated here under fair use. Their use in this slide deck does not change or alter their licensing.

## Slide 17: Sign Magnitude Representation
Binary to Decimal Examples
0110 10102SM
+ 110 1010 2
1011 00102SM
- 011 0010 2
+ (64+32+8+2)10
+ 10610
- (32+16+2)10
- 5010
Notes: Recall subscript 2 was for unsigned binary.
Have them do the negative one.

## Slide 18: Sign Magnitude Representation
Decimal to Binary Example (Positive base 10 Value)
  Interpret sign bit, then use n-1 bit unsigned value.
7310
0 __*26 +__*25 +__*24 +__*23 +__*22 +__*21 +__*20
0 1*64 +__*32 +__*16 +__*8 +__*4 +__*2 +__*1
73
-64
9
0 1*64 + 0*32 + 0*16 + 1*8 +__*4 +__*2 +__*1
0 1*64 + 0*32 + 0*16 + 1*8 +_0*4 +_0*2 +_1*1
7310 = 0100 10012SM
- 8
1
- 1
0
positive

## Slide 19: Sign Magnitude Representation
Decimal to Binary Example (Negative base 10 Value)
  Interpret sign bit, then use n-1 bit unsigned value.
-5210
1 __*26 +__*25 +__*24 +__*23 +__*22 +__*21 +__*20
52
-32
20
-16
4
- 4
0
-5210 = 1011 01002SM
Negative
5210 = 011 01002
Notes: Have them do the negative one?

## Slide 20: Two’s Complement Representation
The most significant bit still indicates the sign of the number.
  0 → positive
  1 → negative
All n bits give the value of:
  Positive numbers using unsigned binary representation.
  Negative numbers using complement of unsigned binary.
    Complement found by flipping the bits and adding 1.
Samples:
0110 10102TC
1001 01102TC
Value in
Unsigned Binary
Positive
Number
Negative
Number
Value is unsigned
binary of the
complement.
Notes: Will use 2TC subscript

## Slide 21: Two’s Complement Representation
Binary to Decimal Examples
0110 10102TC
+ 0110 1010 2
1011 00112TC
0100 1100
+ 1
- 0100 1101 2
+ (64+32+8+2)10
+ 10610
- (64+8+4+1)10
- 7710
Negative. So, use
complement to find
positive (i.e. flip bits and add 1)
Positive. So, exactly the same as unsigned binary
Now same as unsigned binary but include -
Notes: actual value represented.

## Slide 22: Two’s Complement Representation
Decimal to Binary Example (Positive base 10 Value)
  Exactly the same as for n-bit unsigned.
9810
0*128 + 1*64 + 1*32 + 0*16 + 0*8 +_0*4 +_1*2 +_0*1
9810 = 0110 00102
98
-64
34
-32
2
- 2
0
9810 = 0110 00102TC

## Slide 23: Two’s Complement Representation
Decimal to Binary Example (Negative base 10 Value)
  Find n-bit unsigned of positive, then flip bits and add 1.
-10210
10210 = 0110 01102
102
-64
38
-32
6
- 4
2
- 2
0
1001 1001
+ 1
1001 10102TC
-10210 = 1001 10102TC
Flip bits and
add 1 to get
the complement.
Notes: If time have them do one….
-88
88 = 64 + 16 + 8 = 0101 1000 (2)
-88
- (0101 1000) = 1010 0111 + 1 = 1010 1000 (2tc)